## Slide 1
When current is flowing in an ordinary metal wire, the magnitude of the average velocity of the electrons is closest to
  A) 1 m/s.
  B) 1 km/s.
  C) 10 m/s.
  D) the speed of light.
  E) 1 mm/s.

## Slide 2
2) When a current flows through a metal wire, the moving charges are
  A) positive metal ions.
  B) negative metal ions.
  C) only electrons.
  D) both protons and electrons.
  E) only protons.

## Slide 3
3) When the current through a resistor is increased by a factor of 4, the power dissipated by the resistor
  A) increases by a factor of 2.
  B) increases by a factor of 16.
  C) increases by a factor of 4.
  D) decreases by a factor of 16.
  E) decreases by a factor of 4.

## Slide 4
4) How much charge must pass by a point in a wire in 10 s for the current inb the wire to be 0.50 A?
A) 2.0 C B) 0.050 C C) 5.0 C D) 20 C

## Slide 5
5) What current is flowing in a resistor if 4.0 × 10^16 electrons pass a point in the resistor in 0.50 s? (e = 1.60 × 10^-19 C)
A) 6.3 A B) 78 A
C) 0.013 A D) 0.31 A

## Slide 6
6) A light bulb operating at 110 V draws 1.40 A of current. What is its resistance?
  78.6 Ω B) 12.7 Ω
  C) 109 Ω D) 154 Ω

## Slide 7
7) A 4000-Ω resistor is connected across a 220-V power source. What current will flow through the resistor?
A) 0.055 A B) 5.5 A
C) 18 A D) 1.8 A

## Slide 8
8) A light bulb operating at a dc voltage of 120 V has a power rating of 60 W. How much current is flowing through this bulb?
2.5 A B) 0.50 A C) 1.0 A
  D) 2.0 A E) 1.5 A

## Slide 9
9) What potential difference is required to cause 4.00 A to flow through a resistance of 330 Ω?
  334 V B) 1320 V
  C) 82.5 V D) 12.1 V

## Slide 10
10) What is the voltage drop across a 5.0-Ω resistor if the current through it is 5.0 A?
  100 V B) 1.0 V
  C) 25 V D) 4.0 V

## Slide 11
11) When unequal resistors are connected in series across an ideal battery,
A) the potential difference across each is the same.
B) the current flowing in each is the same.
C) the equivalent resistance of the circuit is equal to the average of all the resistances.
D) the equivalent resistance of the circuit is less than that of the smallest resistor.
E) the same power is dissipated in each one.

## Slide 12
12) As more resistors are added in parallel across a constant voltage source, the power supplied by the source
  A) increases.
  B) does not change.
  C) decreases.
  D) increases for a time and then starts to decrease.

## Slide 13
13) Two 4.0-Ω resistors are connected in parallel, and this combination is connected in series with 3.0 Ω. What is the equivalent resistance of this system?
  5.0 Ω B) 11 Ω
  C) 7.0 Ω D) 1.2 Ω

## Slide 14
14) A 2.0-Ω resistor is in series with a parallel combination of 4.0-Ω, 6.0-Ω, and 12-Ω resistors. What is the equivalent resistance of this system?
  24 Ω B) 4.0 Ω
  C) 2.7 Ω D) 1.8 Ω

## Slide 15
15) A 100-V DC signal is applied to a series circuit composed of four equal resistors 10 Ω each. What is the voltage across each resistor?
  10 V B) 50 V C) 15 V
  D) 25 V E) 20 V

## Slide 16
16) A 10.0 V battery is connected across two resistors in series. If the resistors have resistances of 840.0 Ω and 590.0 Ω, what is the voltage drop across the 590.0 Ω resistor?
  7.0 V B) 5.9 V
  C) 4.1 V D) 14 V

## Slide 17
17) Three resistors of 12, 12, and 6.0 Ω are connected in series. A 12-V battery is connected to the combination. What is the current through the battery?
  0.10 A B) 0.40 A
  C) 0.30 A D) 0.20 A

## Slide 18
18) A 14-A current flows into a series combination of a 3.0-Ω and a 4.0-Ω resistor. What is the voltage drop across the 4.0-Ω resistor?
A) 56 V B) 38 V C) 42 V D) 98 V

## Slide 19
19) A 22-A current flows into a parallel combination of a 4.0-Ω, 6.0-Ω, and 12-Ω resistors. What current flows through the 6.0-Ω resistor?
  7.3 A B) 3.7 A
  C) 18 A D) 11 A

## Slide 20
20) Two resistors of 5.0 and 9.0 Ω are connected in parallel. A 4.0-Ω resistor is then connected in series with the parallel combination. A 6.0-V battery is then connected to the series-parallel combination. What is the current through the 4.0-Ω resistor?
  0.53 A B) 0.83 A
  C) zero D) 0.30 A

## Slide 21
21) Two resistors of 5.0 and 9.0 Ω are connected in parallel. A 4.0-Ω resistor is then connected in series with the parallel combination. A 6.0-V battery is then connected to the series-parallel combination. What is the current through the 5.0-Ω resistor?
  0.30 A B) 0.83 A
  C) zero D) 0.53 A

## Slide 22
1) E
2) C
3) B
4) C
5) C
6) A
7) A
8) B
9) B
10) C
11) B
12) A
13) A
14) B
15) D
16) C
17) B
18) A
19) A
20) B
21) D